## Slide 1: Preliminary experimental studies on coalescer efficiency for liquid-liquid separation
Igor Matteo Carraretto
Department of Energy, Politecnico di Milano

## Slide 2
Objective of the work:
Procedure:
Preliminary characterization of a coalescer operations for the regeneration process (see next slide)
Experimental campaign with a commercial mesh and polymer
RES
FO
Introduction

## Slide 3
Full Desolination plant
Nanofiltration
Coalescer
FO membrane
Water storage
Y
Direct two tanks Thermal Energy Storage (TES)
Air Cooled unit
solar tower
receiver
X
Heliostat field
Turbine
generator
Primary heat exchanger
High temperature recuperator
Low temperature recuperator
pump
Compressor
(only for recompressed cycle)
recuperator
Solar plant
tCO2 –mix power plant
Desalination plant
1
2
3
4
5
E
F
G
H
C
D
A
B
Condenser
I

## Slide 4
Draw agent: PAGB2000
Thermoresponsive co-polymer
Regeneration process: diluted and concentrated phases are obtained
Draw agent and FO plant proposed
Nanofiltration
Coalescer
FO membrane
Water storage
Air Cooled unit
Condenser
recuperator
Desalination plant
E
F
G
H
C
D
A
B
I

## Slide 5
Laboratory set-up
Tank
Centrifugal Pump
HEx
Electric Heaters
Coalescer
Air cooler

## Slide 6
Methodology for efficiency determination
Collect three samples of diluted and concentrated phases, with a time step of 15 minutes
Wait until samples are cooled
Measure the concentration using the refractometer
Compute average and standard deviation
0.30
0.40
0.50
0.60
55
60
65
70
75
80
4
6
8
10
12
Operating conditions:
Wait for the steady state
Choose a new operating condition
Objective: find a correlation between and where
Concentration measurement:

## Slide 7
Concentration measurements

## Slide 8
Concentration measurements
Higher flow rates lower the fluid residence time, decreasing diluted phases quality
Temperature is the most significant parameter concerning coalescer performances
The initial draw concentration has negligible impact on the coalescer performance

## Slide 9
Concentration measurements to efficiency

## Slide 10
Coalescer efficiency: fitting surfaces
: phase diagram equation
Cin [%] | MARD [%] | MRD [%] | C1 [] | C2 [min] | C3 []
30 | 7.98 | -0.56 | 1.45 | 4.77 | 7.19
40 | 8.08 | 0.24 | 0.38 | 5.21 | 4.38
50 | 5.86 | 0.34 | 0.26 | 5.83 | 4.21
60 | 4.46 | 0.35 | 0.25 | 4.82 | 4.13
Cin [%] | MARD [%] | MRD [%] |  | C2 [min] | 
30 | 7.98 | -0.56 | 1.45 | 4.77 | 7.19
40 | 8.08 | 0.24 | 0.38 | 5.21 | 4.38
50 | 5.86 | 0.34 | 0.26 | 5.83 | 4.21
60 | 4.46 | 0.35 | 0.25 | 4.82 | 4.13

## Slide 11
Coalescer efficiency: fitting surfaces
: phase diagram equation

## Slide 12
Conclusions
Characterization of the effectiveness of a coalescer for liquid-liquid separation
A coalescer employing a thermo-responsive polymer can be deployed for its regeneration
The thermo-responsive polymer PAGB2000 was tested
The experiments investigated the coalescer under various operating conditions, including initial solution concentrations, regeneration temperatures, and flow rates
The coalescer has a very high separation efficiency (e > 90%)
  It increases as Temperature increases
  It decreases as the Flow-rate is reduced
An efficiency expression was derived starting from a typical efficiency expression of mass transfer
Future research will focus on evaluating performance using alternative thermo-responsive draw agents and metal meshes

## Slide 13
This research activity was carried out within NEST and DESOLINATION projects
NEST - Network 4 Energy Sustainable Transition (D.D. 1243 02/08/2022, PE00000021) and received funding under the National Recovery and Resilience Plan (NRRP), Mission 4 Component 2 Investment 1.3, funded from the European Union - NextGenerationEU
The DESOLINATION project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement #101022686
This presentation reflects only the authors’ views and opinions, neither the European Union nor the European Commission can be considered responsible for them

## Slide 14
Thank for your attention!
Preliminary experimental studies on coalescer efficiency for liquid-liquid separation
I M Carraretto, D Scapinello, R Bellini, L P M Colombo, L Molinaroli and G Manzolini
igormatteo.carraretto@polimi.it