## Slide 1: Non solo energia: il progetto H2020 Desolination
Gioele Di Marcoberardino – Università degli Studi di Brescia
Il Ruolo dell’Ingegneria nella Transizione verso il Futuro
VII Convegno del Dipartimento di Ingegneria Meccanica ed Industriale

## Slide 2: Motivation
Call: H2020-LC-SC3-2020-NZE-RES-CC
Efficient combination of Concentrated Solar Power and desalination (with particular focus on the Gulf Cooperation Council (GCC) region)
Seawater desalination plant coupled with
concentrated solar power plant (CSP)
Need to develop technologies capable of producing drinking water from sea water
Types of water | Amount [%]
Sea water | 
Glaciers | 
Fresh water | 
Types of water | Amount [%]
Sea water | 
Glaciers | 
Fresh water | 
Why?
DESALINATION UNIT
CSP UNIT
concentrated solar power plant
recompressed CO2 supercritical cycle
solar driven
advanced features
Forward Osmosis (FO)
Advanced CSP plant
opposed to Reverse Osmosis (RO)
exploits low grade/waste heat
low electrical consumptions expected
purification step: DCMD or NF
seawater as feed

## Slide 3: The concept
Symbiosis: No energy waste, No efficiency penalty
Sea Water
FO
ZLD
Pure Water
Metal recovery
Desalination section – FO+MD
MD
CO2 blends in power block
  higher performance
  lower costs
Forward Osmosys and membrane distillation:
  low energy cost
Lower cost of electricity < 90 €/MWh
Lower cost of water < 1 €/m3
Reduced CO2 emissions by >30%
C
O
O

## Slide 4: Options for combining solar energy and desalination
Desalination Technologies
Evaporation & Condensation
Filtration
Mechanical process
Thermal process
Mechanical Vapor Compression (MVC)
Multi-Effect Distillation (MED)
Multi-Stage Flesh (MSF)
Solar Still Distillation (SSD)
Thermal Vapor Compression (TVC)
Humidification Dehumidification (HDH)
Solar Chimney (SC)
Reverse Osmosis (RO)
Forward Osmosis (FO)
Nanofiltration (NF)
Ion-Exchange Resin (IXR)
Membrane Distillation (MD)
Electro-Dialysis (ED)
Capacitive Deionization (CDI)
Driving Force
Driving Force
Water flux
REVERSE OSMOSIS
FORWARD OSMOSIS

## Slide 5: Why DESOLINATION? - Advantages of tCO2-blends and Forward Osmosis
Two phase
One phase
A
A
B
B
Heat rejection curve from tCO2 cycles
Draw solution + water phase diagram
Win-Win
C
D
D
C

## Slide 6: Why DESOLINATION?
PV + RO
+28% area

## Slide 7: The Consortium: 21 Partners
SMEs
Large Companies
Research Centre
Universities

## Slide 8: Demonstration site

## Slide 9: From the concept to the demonstration
Sea Water
FO
ZLD
Pure Water
Metal recovery
Desalination section – FO+MD
MD
1.8 MWel
>2300 hours
TRL 4
TRL 7
>2 m3/day

## Slide 10: UNIBS role and activities
Thermal stability test
Vapour-liquid equilibrium test
Thermodynamic properties
EoS calibration
CO2 BLENDS
Dopants identification
Promising
dopants
Long term
thermal stability test
Identification of the working fluid for the pilot power plant
Working fluid TDN properties definition for the components design
Material compatibility test at the maximum operating temperature to select the proper materials

## Slide 11: UNIBS role and activities
Transcritical cycle
SCARABEUS concept
Supercritical cycle
CO2 BLENDS
Dopants identification
Identification of dopants for blending CO2
An ideal dopant should:
Be Thermally stable at high temperature (550°C)
Have a critical temperature > 100°C
Other dopant characteristics:
Melting point < T ambient
 avoiding pipes clogging at ambient temperatures
Solubility with CO2
High molecular complexity
Environmental friendly (if possible)

## Slide 12: UNIBS role and activities: Thermal stability definition and procedure
Main apparatus

## Slide 13: UNIBS role and activities: Thermal stability definition and procedure
Thermal stability test procedure (static method)
FRESH MIXTURE
Definition of reference isochoric line (and its uncertainty)
THERMAL STRESS
100 h at different temperatures
COMPARISON &
DEVIATION IDENTIFICATION
Graphical method
New isochoric line after thermal stress VS reference behavior
Gas phase
p,T
measurements
Chart: TEMPERATURE (°C)
| -80.649799999999999 | -66.119799999999998 | -55.044899999999998 | -46.949199999999998 | -38.228200000000001 | -28.841899999999999 | -18.765599999999999 | -8.0012500000000006 | 3.40693 | 15.3545 | 27.6569 | 40.030999999999999 | 52.080300000000001 | 63.284799999999997 | 72.9953 | 80.438800000000001 | 84.763599999999997 | 85.208600000000004
DEW | 0.019203 | 0.062543 | 0.1361 | 0.22721 | 0.37702 | 0.62087 | 1.0128 | 1.6326 | 2.5934 | 4.047 | 6.1815 | 9.2074 | 13.3213 | 18.644 | 25.1265 | 32.4278 | 39.7914 | 46.0333
RIF | 9.0877 | 10.5376 | 13.5044 | 15.5746 | 16.7725 | 17.9397 | 18.4787 | 19.0335 | 19.5995 | 20.1397 | 20.6282 | 21.1314 | 21.6505 | 22.3528
AFTER 100 h @ 400 °C | 10.0967 | 11.5301 | 13.6442 | 15.568 | 16.6764 | 17.7593 | 18.3471 | 18.8878 | 19.407 | 19.9224 | 20.4316 | 20.9403 | 21.4463 | 21.9506 | 0 | 0 | 0 | 0 | 0
AFTER 100 h @ 450 °C | 10.1667 | 11.4211 | 13.4828 | 15.3813 | 16.567 | 17.6737 | 18.2082 | 18.7271 | 19.2373 | 19.8184 | 20.3655 | 20.8703 | 21.3706 | 21.8755 | 0 | 0 | 0 | 23.9717 | 0
AFTER 100 h @ 500 °C | 10.2582 | 11.576 | 13.7223 | 15.4673 | 16.7629 | 17.8283 | 18.328 | 18.9739 | 19.5262 | 20.0443 | 20.5994 | 21.1144 | 21.6189 | 22.1204 | 0 | 0 | 0 | 24.3062 | 0
AFTER 100 h @ 550 °C | 16.5769 | 18.0682 | 19.5126 | 20.9084 | 22.2532 | 23.5681 | 24.2199 | 24.8505 | 25.4848 | 26.124 | 26.7511 | 27.3874 | 28.0188 | 28.6389 | 0 | 0 | 0 | 0 | 0
Two phase (VLE)

## Slide 14: UNIBS role and activities: material compatibility
Material Compatibility Tests
First Campaign: Samples in Welded Cylinder
CO2 blend at 550°C for >500 h
Materials
Ni-alloys
other selected materials….
After Long-term thermal stress test  sample analysis (mass gain, SEM, optical microscope)
Second Campaign: Samples in Flanged Cylinder
CO2 blend at 550°C for >2000 h
At high temperature, material compatibility info are fundamental
Microstructural analysis by means of MeF3 optical microscope equipped with LAS4.12 software for image analysis

## Slide 15: Overall project cost
Call: H2020-LC-SC3-2020-NZE-RES-CC
Efficient combination of Concentrated Solar Power and desalination (with particular focus on the Gulf Cooperation Council (GCC) region)
Overall project budget: +15 M€
International collaboration increases the impact
Private investments are required
Projects are typically budget constraint

## Slide 16: Project Milestones and Timelines
2021
Project Inception
The DESOLINATION project kicks off with a focus on integrating CSP and desalination technologies to create sustainable solutions for water and energy
2022-2023
Innovative Thermodynamic Solutions
Groundbreaking work on CO2 mixtures for thermodynamic cycles leads to effective and efficient coupling of CSP with CO2-mixtures power cycles and forward osmosis desalination system
Experimental campaign on the coalescer using a solution of water and PAGB2000, obtaining an expression of the separation efficiency, to be deployed in the simulations.
2024
Pilot Plant development
Development of the pilot plant site, marking a significant step towards real-world application and testing of DESOLINATION technologies.
2025
Technology Demonstration
The integration of both existing and next generation CSP cycles will be implemented in the King Saudi University facility to allow testing in a real environment.
2026
Commercialization and Market Uptake
DESOLINATION partners will work on defining a clear roadmap from TRL 6 to TRL 9, ensuring a strong market uptake and exploitation strategy for the developed technologies.

## Slide 17: Acknowledgements
The DESOLINATION project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement N° 101022686
www.desolination.eu – LinkedIn Desolination
gioele.dimarcoberardino@unibs.it